## Slide 1
STM32 – Accelerometer
Federica Villa

## Slide 2: MEMS accelerometer
Connected to the I2C bus
address: 010100+ 0  0101000 (7 bit address) [LIS2DE] 001100+ 0  0011000 [LIS2DE12]
slave
Write protocol: Write register sub-address, register content in a single operation
Read protocol: 1) Write register sub-address 2) Read register content
Multiple read protocol: 1) Write sub-address of the first register to be read, with MSB set to ‘1’ (refer to datasheet page 22 – auto-increment) 2) Read multiple registers (in sequence)
Possible board variants

## Slide 3: Project 01a
Read the acceleration measured by the accelerometer and send it to a remote terminal every 1 second.

## Slide 4: Aim of the project
Identify which accelerometer is installed on your board. You can exploit the return value of the HAL_I2C_Master_Transmit().
Acquire the x, y, z acceleration and send the 3 values to a remote terminal, about every 2 seconds.
The value of acceleration must be expressed in g, with a precision of 0.01 g and the correct sign.
The full-scale range must be +/- 2 g.
The output format of the data must be like the one in the example:
X: +0.05 g Y: -0.22 g Z: +1.00 g

## Slide 5: Project hints
Configure the microcontroller to enable the I2C1 peripheral, as in slides 09.
Initialize the accelerometer setting the correct registers to enable normal mode operation, with all 3 channels active, 1 Hz update rate, no high pass filter and ± 2g Full Scale range. Refer to the datasheet.
Acquire the acceleration values of all 3 axis every second and send it to the PC using UART. Use the while(1) loop and HAL_Delay().
Compile the code

## Slide 6: Project 01b
Read the acceleration measured by the accelerometer and send it to a remote terminal every 1 second.
Using timer interrupts and UART DMA.

## Slide 7: Project hints
Start from the previous project.
Use a timer to generate an interrupt every second.
Within the timer callback, acquire the acceleration values of all 3 axis. Send all the data to the PC via UART using DMA in a single operation. See slides 06 for the correct setup.
Compile and debug the code

## Slide 8: Project 01c
Read the acceleration measured by the accelerometer and send it to a remote terminal every 1 second.
Using timer interrupts, I2C DMA and UART DMA.

## Slide 9: Project hints
Start from the previous project. Setup the I2C1_RX DMA and enable I2C interrupts.
In the timer callback, acquire the data from the device exploiting the auto-increment feature of the sub-address (see LIS2DE datasheet, page 22). Perform an I2C read with DMA to read in a single operation the OUT_X, OUT_Y and OUT_Z registers. How many bytes to you have to transfer?
Within the HAL_I2C_MasterRxCpltCallback create the string and send it to UART, again using a single DMA Transmit operation.
Compile the code

## Slide 10: LIS2DE
address: 010100+ 0  0101000 (7 bit address) [LIS2DE] 001100+ 0  0011000 [LIS2DE12]
slave
8-bit sub-address (SUB) is transmitted: the 7 LSb represent the actual register address while the MSb enables address auto increment
CTRL_REG1 (20h): 0001 1111 (1 Hz, enable X Y Z)
CTRL_REG2 (21h): 00 00 0000 (disable HP filter)
OUT_X_H (29h)
OUT_Y_H (2Bh)
OUT_Z_H (2Dh)
Possible board variants